## Slide 1: Iskorištavanje voda

## Slide 2: Raspodijela stanovništva i zaliha vode

## Slide 4: Voda se koristi za:
Kupanje
WC
Čišćenje
Priprema hrane
Hlađenje
Zaštita od požara
Industrijske svrhe
Voda za piće = pitka voda
©iStockphoto.com
Notes: Today, almost all commercial, industrial, or residential structures must have a water supply. Water is also used for such things as bathing, toilets, cleaning, food preparation, cooling, fire protection, and industrial processes.

## Slide 5: Distribucija zaliha vode
Notes: Some civil engineers are responsible for designing systems that provide a reliable and clean water supply.
A water supply system begins at a water source.
Water is transported to a treatment facility where the water is treated to ensure the supply is safe.
Once treated, the water is transported to a storage facility (for example, a water tower) where it is stored for future demand.
When a water faucet is opened or a fire sprinkler is activated, water is transported through the distribution system to the consumer.

## Slide 6: Izvori vode
Vodonosnici (podzemne vode) Primarni izvor pitke vode Porozne konsolidirane stijene ili nekonsolidirano tlo Podzemna voda ispunjava prostore Bunari i pumpe za uklanjanje vode
Aquifer
Courtesy USGS at http://pubs.usgs.gov/circ/circ1139/htdocs/boxa.htm
This image was reproduced from groundwater.org with the permission of The Groundwater Foundation. © 2010 The Groundwater Foundation. All Rights Reserved

## Slide 7: Izvori vode
  Jezera , rezervari i rijeke
  Brane na rijekama za rezervare
  Rezervari skladište vodu tijekom obilnih kiša
Courtesy NASA http://www.ghcc.msfc.nasa.gov/surface_hydrology/water_management.html
Courtesy USDA http://www.ks.nrcs.usda.gov/news/highlights/2006_april.html
Lake Tuscaloosa Dam
©iStockphoto.com

## Slide 8: Tretiranje vode
Količina tretmana ovisi o kvaliteti izvora Podzemna
voda zahtijeva manje obrade nego površinske vode
Tretiranje vode za grad Salem
Courtesty USGS http://pubs.usgs.gov/fs/2004/3069/
Notes: The method of water treatment and the size of the plant are dependent on the quality of the water supply and the water demand. In general ground water requires less treatment than surface water because surface water is exposed to more contaminants. Water from some private well sources may require no treatment.

## Slide 9: Pohrana vode
Pumpanje u vodeni toranje
  zalihe
  Vodeni pritisak
    psi
    1 psi = 2.31 stopa vode
NOAA http://www.csc.noaa.gov/alternatives/infrastructure.html
Notes: Treated water is pumped to a storage tank. Storage tanks are often elevated. A storage tank serves two purposes.
It stores the water until it is needed, which reduces the peak demand on the treatment facility.
Elevated water tanks create pressure in the water distribution system.

## Slide 10: Sustav distribucije vode
Sastoji se od vodovoda, spojnih elemenata, ventila, servisnih linija, brojila i hidranata
Sustav petlje poželjniji od sustava ogranaka Izolacijski ventili Voda teče u više smjerova
Sustav petlje
Sustav ogranka
Notes: The water distribution system includes all of the water lines and components attached to the water lines.
There are basically two different distribution system configurations: Loop systems and branch systems.
Loop systems are more desirable because they provide redundancy. If a leak occurs in a loop system, installed isolation valves can be used to close off a small area near the leak but allow the remainder of the system to continue to provide water. In a branch system, the entire system must be shut down to repair a leak.
In addition, the loop system allows water to flow from more than one direction which can reduce the negative effect felt in a branch system when upstream demand reduces pressure and flow rate.

## Slide 11: Sustav distribucije vode
Tipična nova cijev sustava
Termoplastično ili nodularno željezo Armirani beton u većim mrežama
Starija cijev sustava Lijevano željezo ili azbestni cement
Tipični tlak raspodjele od 65 - 75 psi
Dizajniran za manje od 150 psi
wikimedia
Notes: New systems are often constructed with thermoplastic or ductile iron piping. Because the efficiency of the system depends on a smooth interior pipe surface, cement linings or coatings are sometimes used to reduce the pitting and corrosion associated with iron pipes. For larger diameter water mains, reinforced concrete pipe is often used.
Cast-iron pipe and asbestos cement pipe have been a popular choice for water distribution systems in the past, so you may encounter these materials when tying into older existing systems.
A distribution system pressure of 65 – 75 psi is often recommended. Pressures over 150 psi can cause leaks and damage to the system.

## Slide 12: Korisnik
Stambeni, poslovni i industrijski objekti stambeni
Min. distribucijski tlak = 40 psi
Maks. distribucijski tlak = 80 psi Ventil za smanjenje tlaka Komercijalni ili industrijski objekti Može zahtijevati viši tlak Pumpe mogu povećati tlak
©iStockphoto.com
©iStockphoto.com
Notes: The water supply system must adequately serve all customers including residential, commercial, and industrial facilities. The water pressure, flow rate, and demand times may vary significantly among users.
For residential consumers, the minimum desirable distribution pressure is 40 psi. A pressure over 60 psi is considered high. Because it increases the flow rate, high water pressure can lead to increased water use (waste) and increased energy use (due to heating the excess water). In addition, high water pressure can damage appliances and fixtures and cause them to wear out more quickly. Codes often require pressure-reducing valves at the service meter when the distribution pressures exceed 80 psi.

## Slide 13: Igrajmo kahoot kviz:
https://create.kahoot.it/details/uses-of-water-and-water-footprint/766ed4bd-88c8-41d9-958f-4b5701636815
http://tiny.cc/ljoa4y